## Slide 1: Thin Layer Interfaces
COMSOL

## Slide 2: Background and Motivation
A layers is considered thin when its thickness is small compared to other dimensions of the structures
Difficult to produce a solid mesh of acceptable quality
Thin Layer feature can be used to avoid meshing
Alternative approximations are available: solid, membrane and spring
Continuity of the displacement and stress fields depends on the layer approximation and material properties

## Slide 3: Solid approximation
Continuity of displacement is not enforced
Continuity of stress is not enforced
Solid approximation

## Slide 4: Membrane approximation
Continuity of displacement is enforced
Continuity of stress is not enforced
Converges to a perfect interface for low values of the interface shear modulus.
Transition from membrane approximation to perfect interface

## Slide 5: Spring approximation
Continuity of displacement is not enforced
Converges to a perfect interface for high values of spring stiffness
Transition from spring approximation to perfect interface