## Slide 1: Linear Magnetic Gear in 2D Axisymmetry

## Slide 2: Construction
Iron backing
Permanent magnets
(blue and red)
High speed armature
Pi = 2 pole pairs
Low speed armature
Po = 11 pole pairs
Iron backing
Stationary steel poles
Ps = 15 pole pairs
Vo
Vi

## Slide 3: Construction
Low speed rotor consists of Iron and 11-pole pair permanent magnets (22 pieces).
The stationary steel poles consists of 15 equally spaced steel pieces.
High speed rotor consists of Iron and 4-pole pair permanent magnets (8 pieces)
Iron Backing
Iron Backing
Permanent Magnets
Stationary Steel Poles
High Speed
Armature
Low Speed
Armature
r=0

## Slide 4: Construction (contd.)
The low speed armature (on the right) consist of 22 permanent magnets (PMs) pieces and a soft iron backing forming a 11-pole pair rotor.
The high speed armature (on the left) consists of 8 PMs pieces and soft iron backing forming a 4-pole pair rotor.
The middle stationary ring consists of 15 steel poles with equally spaced airgaps in between.
The number of pole pairs for all three section are selected such that the torque ripple is minimum.
The torque/speed relation is given in the next slide.

## Slide 5: Gear Ratio and Torque Transmission
ωl = Speed of low speed rotor
ωh = Speed of high speed rotor
ωs = Speed of steel poles.
The relation between the speeds of the three rotors is:
ω
pl = Number of pole pairs in low speed rotor = 11
ph = Number of pole pairs in high speed rotor = 4
ps = Number of pole pairs in steel pole rotor = 15
Keeping the steel poles stationary i.e. ωs =0
ω
Since, ph - ps= -pl
ωG12
Where, G12 is called gear ratio.
These ripples are primarily due to the cogging torque created from the interaction of the PM motors and the stationary steel poles-pieces. The armature with less pole pairs usually has a higher cogging torque (armature on the left). The parameter that is used for minimizing these cogging torque is called a cogging factor given by:
C
Here, LCM is a “least common multiple”. The best configuration is obtained for Cf = 1.

## Slide 6: Parameters

## Slide 7: Geometry
Note 1: Form three Unions for high speed armature, low speed armature and stationary steel regions.
Note 2: The Form an Assembly option is needed here to create geometric discontinuity which is used later to allow the mesh around the rotor to slide against the mesh around the stator. Two separate Identity Pairs are created (as shown in next two slides).

## Slide 8: Identity Pair I

## Slide 9: Identity Pair 2

## Slide 10: Periodic Condition 1
NOTE: The identical mesh should be used at the source and destination boundaries of the periodic boundary condition.

## Slide 11: Magnetic Potential 1Using General Extrusion 1

## Slide 12: Magnetic Potential 2using General Extrusion 2

## Slide 13: Perfect Magnetic Conductor

## Slide 14: Moving Mesh: Fixed Mesh Part

## Slide 15: Moving Mesh: Prescribed Deformation High Speed Armature

## Slide 16: Moving Mesh: Prescribed Deformation Low Speed Armature

## Slide 17: Solver Settings
NOTE: “Stationary” step is necessary to model the magnetic fields produced by the Permanent Magnets at t=0[s]. The results from the “Stationary” study will automatically be used as the initial condition for the “Time Dependent” study step. See the following Knowledge Based Entry for detail:
http://www.comsol.com/support/knowledgebase/1127/
# Add “Time Dependent” solver
# Right click “Study 1” -> “Show Default Solver”

## Slide 18: Results: Magnetic Flux Density
Notes: The model was solved for a single pole, but the results are displayed for other two poles before and after the actual one that is solved.

## Slide 19: Results: Magnetic Field, Radial Component
Notes: The model was solved for a single pole, but the results are displayed for other two poles before and after the actual one that is solved.

## Slide 20: Results: Magnetic Flux Density
The volume plot for magnetic flux density norm and the contour plot for magnetic flux density radial component.

## Slide 21: Result: Electromagnetic Forces on the High Speed and Low Speed Armatures
Low speed armature
High speed armature

## Slide 22: Result: Electromagnetic Force, Fz on the High Speed Armature

## Slide 23: Result: Electromagnetic Force, Fz on the Low Speed Armature

## Slide 24: Results: Magnetic Flux Density in the Airgap adjacent to High Speed Armature
This is the plot for r-component of magnetic flux density in the airgap between the high speed rotor and steel poles along the length of the armature at time t=0s.

## Slide 25: Results: Magnetic Flux Density in the Airgap adjacent to Low Speed Armature
This is the plot for r-component of magnetic flux density in the airgap between the low speed rotor and steel poles along the length of the armature at time t= 0s.