## Slide 1: Modeling of Free Surfaces in COMSOL Multiphysics® A Comparison of Level Set, Phase Field, and Moving Mesh Methods

## Slide 2: Free Liquid Surfaces
Three different approaches:
Level Set
Phase Field
Moving Mesh

## Slide 3: Level Set and Phase Field Methods
The free surface is an isosurface of either the level set or the phase field function, both denoted f
The level set or phase field functions, f, are advected by the fluids’ velocity vectors
The value of f determines the properties of the fluids, e.g. if it is the liquid or the gas

## Slide 4: Level Set and Phase Field Methods
The model equation (the nonconservative form):
The source term, F, differs in the two methods
The velocity vector The phase field or level set function A source term

## Slide 5: Level Set and Phase Field Methods
Fluid Properties with volume averaging:
The example is for the level set function but the analogy is valid for the phase field function
Density Dynamic Viscosity

## Slide 6: Level Set and Phase Field Methods
Surface tension introduced as a source term in the momentum equations:
Level set uses the curvature of the isosurface to compute the source
Phase field adds a force computed from the chemical potential close to the isosurface to account for surface tension

## Slide 7: The Example Problem
Add gravity
Add reference point with a pressure point constraint
Use Navier slip condition for the walls

## Slide 8: Results: Level Set vs Phase Field

## Slide 9: Phase Field

## Slide 10: Phase Field with Topology Changes

## Slide 11: Adaptive Meshing

## Slide 12: Free Surface with Moving Mesh
The displacement velocity of the free surface is obtained as the fluid’s velocity
The solution to the moving mesh equations smoothly displaces the mesh nodes at the surface and inside the bulk of the fluid
The Navier-Stokes equations are solved on a moving frame fully coupled to the mesh equations

## Slide 13: Free Surface with Moving Mesh
Benefits:
  Forces on the surface, such as surface tension, can be added directly at the surface as boundary conditions
  Computationally efficient since there is the option to avoid computing the velocity and pressure fields in the gas phase
Downside:
  Cannot handle topology changes

## Slide 14: Moving Mesh vs Phase field

## Slide 15: Moving Mesh vs Phase field

## Slide 16: Conclusions for Modeling of Free Surfaces
Moving mesh is the best choice if there are no topology changes
Phase field is the best choice for modeling free surfaces with surface tension effects and where topology changes occur
Level set is the most computationally effective method when surface tension is less important