## Slide 1: Fatigue Analysis of a Wheel Rim

## Slide 2: Model Background
High-cycle fatigue is simulated in a wheel rim.
The rotating wheel is subjected to both a fixed in space and a traveling load.
The concept of submodeling is utilized to capture the stress distribution in the complex geometry.

## Slide 3: Submodeling
In submodling, an analysis is preformed in two steps.
First you solve the complete model with a mesh, which is sufficient to capture the stiffness of the structure.
In a second analysis you create a local model of the region around the stress concentration with a fine mesh, and solve it using the displacements from the global model as boundary conditions.

## Slide 4: Fatigue Evaluation
Since the wheel rim is intended for a long lifetime, the design is made against high-cycle fatigue.
The fatigue prediction is based on the Findley stress-based fatigue criteria.
The material parameters are computed from two standard fatigue tests:
  pure tension
  pure axial loading